## Slide 1
Université Mohammed VI Polytechnique
School of applied and engineering physics.
School of applied and engineering physics.
Ibtissam Ait Haddou
Khawla NAJMI
May 11, 2026
Supervised by: Prof. Hicham Atmani
Nuclear Physics Applications in Medicine
Physics Foundations & Technological Challenges
Marime Charafi
Korotimi Syla Sangare
Realized by :

## Slide 2
Nuclear Physics Applications in Medecine
11/05/2026
Outline :
Introduction
Nuclear Imaging
Nuclear Therapy
Current Challenges
1
2
3
4

## Slide 3
Introduction
11/05/2026
1) INTRODUCTION TO NUCLEAR MEDICINE :
Nuclear medicine uses radioactive isotopes for:
Medical Imaging
Therapy (cancer treatment)
In conventional X-rays:
The machine emits radiation
In nuclear medicine:
The patient becomes the source of radiation
Applications:
Cancer detection
Thyroid disorders
Bone imaging
Cardiac imaging
Functional imaging

## Slide 4
Physics Foundations
11/05/2026
A) Radioactivity and Type of nuclear decay:
Radioactivity : The spontaneous transformation
of an unstable nucleus intro a more stable nucleus

## Slide 5
Physics Foundations
11/05/2026
Radiation interacts with tissues mainly through:
Ionization
Excitation of atoms
Main photon interactions:
Photoelectric effect
Compton scattering
B) Interaction of radiation with bioligical matter:
Alpha particles | Beta particles | Gamma rays
very high ionization very short range | moderate penetration scattering in tissues | highly penetrating detected outside the body

## Slide 6
Physics Foundations
11/05/2026
C) Radiation dosimetry :

## Slide 7
Physics Foundations
11/05/2026
D) Criteria for choosing medical radioisotopes:
Half life | Type of radiation | Photon energy | Biological targeting
Short enough to reduce patient dose Long enough for examination or therapy | γ emitters for imaging β or α emitters for therapy | Typically 100–200 keV for imaging | Must accumulate in target organ
Tc-99m F-18 PET scan I-131 (for thyroid therapy)
(imaging)

## Slide 8
Nuclear Imaging
11/05/2026
2) Nuclear Imaging
Injection of the Radiotracer
External Detection and Image Formation
Radioactive Emission
Distribution in the Body
The Principles of Nuclear Imaging :
Nuclear imaging sees function :
Is the tumor metabolically active?
Is the organ working properly?
Where has cancer spread?
Nuclear Imaging techniques :
Planar Scintigraphy
SPECT (Single Photon Emission Computed Tomography)
PET (Positron Emission Tomography)
Other techniques see structure :
X-ray / CT → shape & bones
MRI → soft tissue detail
Figure 1

## Slide 9
Nuclear Imaging
11/05/2026
Scintigraphy :
Latin scintilla meaning spark
Oldest and simplest
flat, 2D image
a) The Radiotracer:
The radioactive atom (called a radionuclide or radioisotope) is attached to the carrier. Its job is to emit gamma rays so the detector can find it.
Radiotracer = Carrier molecule + Radioactive atom
Carrier : sugar, hormone, antibody
Targets a specific organ
property | Value
Type of emission | Gamma rays only (140 keV)
Half-life | 6 hours
Energy | 140 keV
Production | From a Mo-99/Tc-99m generator
A) Planar Scintigraphy

## Slide 10
Nuclear Imaging
11/05/2026
Layer 2: NaI(Tl) Crystal
γ ray → 1,000–3,000 light flashes
Scintillation principle
Anger Logic (1958)
Each PMT gets different light intensity
Position calculated by weighted average X = Σ(Sᵢ · xᵢ) / ΣSᵢ
Millions of dots → 2D map
Layer 3: PMTs (37–91 tubes)
Light → electrical signal
Amplification ×1,000,000
Limitations
2D only : no depth info
Attenuation : deep = weak signal
b) The Gamma Camera (Anger Camera):
Radiotracer emits gamma rays in all directions. The gamma camera must:
Capture those gamma rays
Determine where each gamma ray came from
Build a 2D image from all those data points
A) Planar Scintigraphy
Layer 1 :Collimator (lead)
Blocks 99.9% of γ rays
Only perpendicular rays pass
Defines image sharpness

## Slide 11
Nuclear Imaging
11/05/2026
SPECT takes scintigraphy and adds 3D reconstruction.
SPECT = Scintigraphy + Rotation + Math
How SPECT Works ?
Step 1: Rotating the Camera
Camera rotates 360° around patient
Takes 60–120 projections at every angle
Step 2 : Reconstruction (algorithms )
FBP : Filtered Back Projection
Projects shadows back from all angles → overlap = object location
Fast but noise-sensitive → streak artifacts
OSEM : Ordered Subset Expectation Maximization
Starts with a guess → compares → refines repeatedly
Slower but cleaner & more accurate → modern standard
SPECT Limitations
Spatial resolution still limited (~8 to 12 mm)
Scan time is long (15 to 45 minutes of rotation)
Sensitivity lower than PET (fewer gamma rays are detected)
Only one gamma ray per decay is detected
B) SPECT (Single Photon Emission Computed Tomography)

## Slide 12
Nuclear Imaging
11/05/2026
C) PET (Positron Emission Tomography)
PET is the most sensitive and highest resolution form of nuclear imaging
a) Positron Annihilation :
1) Positron emission
¹⁸F → ¹⁸O + β⁺ + νₑ
2) Annihilation
β⁺ + e⁻ → γ (511 keV) + γ (511 keV)
Figure 1 : A PET scanner is a ring of thousands of small detector crystals
A
If detector A and detector B both register a 511 keV gamma ray within ~5–10 nanoseconds of each other
the system concludes: an annihilation occurred somewhere along the line connecting A and B (called a "line of response" or LOR)This is recorded as one valid event
By recording millions of LORs from all directions around the ring
the computer can use the same tomographic reconstruction algorithms (OSEM) as SPECT to build a 3D image
b) The PET Detector Ring , Coincidence Detection

## Slide 13
Nuclear Imaging
11/05/2026
c) The Key Radiotracer : ¹⁸F-FDG (fluorodeoxyglucose)
The most widely used PET radiotracer in the world
d ) SUV (Standardized Uptake Value)
For exemple : SUV > 2.5 in a lung nodule is suspicious for malignancy.
¹⁸F : Fluorine-18 | FDG : Modified Glucose
Positron emitter (β⁺) | Identical to real glucose
Half-life : 110 min | Enters cells → gets trapped
Produced by cyclotron | Cannot leave → accumulates
Why it works for cancer
Warburg effect : tumors consume 5 to 10× more glucose
Clinical uses
Cancer staging & recurrence
Chemotherapy monitoring
Brain : Alzheimer's, epilepsy
SUV
C) PET (Positron Emission Tomography)

## Slide 14
Nuclear Therapy
11/05/2026
3) THERAPEUTIC APPLICATIONS :
how do we use radiation to destroy cancer cells while protecting healthy tissue as much as possible?
External Beam Radiotherapy (EBRT)
Brachytherapy
Targeted Radionuclide Therapy (TRT)
maximize dose to the tumor, minimize dose to healthy tissue.

## Slide 15
Nuclear Imaging
11/05/2026
B) External beam radiotherapy
Principle
A machine outside the patient generates a beam of radiation and points it at the tumor. The beam enters the body, crosses healthy tissue, hits the tumor, and depending on the type of radiation may or may not exit on the other side.

## Slide 16
Nuclear Imaging
11/05/2026
B) External beam radiotherapy
1. Photon Therapy (X-rays)
Interaction | Energy range | What happens
Photoelectric effect | < 0.1 MeV | Photon absorbed completely, ejects electron
Compton scattering | 0.1–10 MeV (dominant in therapy) | Photon scatters off electron, both continue
Pair production | > 1.022 MeV | Photon creates electron + positron pair
The most common machine is called a LINAC (Linear Accelerator). It accelerates electrons to very high energies (6–18 MeV), then slams them into a tungsten target. The electrons suddenly decelerate and produce X-rays this process is called bremsstrahlung The X-ray beam enters the patient's body and deposits its energy mainly through three interactions with tissue:

## Slide 17
Nuclear Imaging
11/05/2026
A) External beam radiotherapy
2 Electron Therapy
Electrons (β⁻ particles) have a short range in tissue a few centimeters because they lose energy quickly by ionizing atoms along their path.This makes them ideal for superficial tumors: skin cancer, chest wall lesions, post-mastectomy treatment. Below about 5–6 cm depth, the dose drops to nearly zero.
3.Hadrontherapy
Proton vs X-ray dose curves
Proton therapy dose diagram

## Slide 18
Nuclear Imaging
11/05/2026
A) External beam radiotherapy
the Bethe-Bloch equation:
Carbon ions (C-12, charge z = 6) lose energy 36 times faster than protons (z² ratio: 6² vs 1²) for the same velocity. This creates a much sharper, more intense Bragg peak.
Carbon Ions vs. Protons ,Relative Biological Effectiveness (RBE)
Linear Energy Transfer (LET):
LET=−dE/dx ​
RBE (Relative Biological Effectiveness):

## Slide 19
Nuclear Imaging
11/05/2026
A) External beam radiotherapy
Feature | Photons (X-rays) | Protons | Carbon ions (C-12)
Bragg peak | No | Yes | Yes, sharper
Exit dose | Yes | Nearly zero | Nearly zero
LET (at tumor) | ~0.5 keV/µm | ~10 keV/µm | ~80 keV/µm
RBE | 1 (reference) | ~1.1 | ~2–3
Best for | Most tumors | Skull base, pediatric | Radioresistant tumors
Clinical centers (2024) | Everywhere | ~120 worldwide | ~15 worldwide

## Slide 20
Nuclear Imaging
11/05/2026
B) Brachytherapy
Principle
INVERSE-SQUARE LAW
Doubling the distance from the source divides the dose by ~4 , neighboring tissues are spared a few millimeters away.
Brachytherapy uses sealed sources
Isotope | Half-life | Energy | Main clinical use
¹⁹²Ir (Iridium-192) | 73.8 days | 380 keV (γ) | HDR: cervix, breast, head & neck
¹²⁵I (Iodine-125) | 59.4 days | 28 keV (γ) | LDR: prostate permanent implant
¹⁰³Pd (Palladium-103) | 17 days | 21 keV (γ) | LDR: prostate (low-grade)
⁶⁰Co (Cobalt-60) | 5.27 years | 1.25 MeV (γ) | HDR alternative to Ir-192
internal radiation therapy where sealed radioactive sources are placed directly into or adjacent to a tumor, providing highly localized, high-dose treatment.

## Slide 21
Nuclear Imaging
11/05/2026
B) Brachytherapy
Brachytherapy is therefore classified by dose rate:
Category | Dose rate | How it works
LDR (Low Dose Rate) | 0.4–2 Gy/h | Seeds implanted permanently; slow continuous irradiation over weeks
HDR (High Dose Rate) | > 12 Gy/h | Source inserted temporarily for minutes; patient goes home same day
PDR (Pulsed Dose Rate) | Pulses of ~0.5 Gy/h | Hourly pulses simulating LDR biology with HDR equipment
Clinical Applications:
Prostate cancer
neck cancers

## Slide 22
Nuclear Therapy
11/05/2026
C) Targeted radionuclide therapy
TRT is a systemic treatment that uses radiopharmaceuticals , radioactive atoms chemically coupled to biological carrier molecules to deliver ionizing radiation selectively to cancer cells.
Principle

## Slide 23
Nuclear Therapy
11/05/2026
C) Targeted radionuclide therapy
Property | ¹³¹I | ¹⁷⁷Lu | ²²³Ra
Particle type | β⁻ + γ | β⁻ + γ | α (+ β, γ chain)
Half-life | 8.05 days | 6.65 days | 11.4 days
Range in tissue | ~2.4 mm | ~1.5 mm | < 0.1 mm
LET | Low (~0.5 keV/µm) | Low–medium | High (~80 keV/µm)
Targeting mechanism | NIS symporter | SSTR₂ receptor (NETs) / PSMA (prostate) | Calcium mimetic → hydroxyapatite
FDA approval | Decades | 2018 (Lutathera) / 2022 (Pluvicto) | 2013 (Xofigo)
Theranostic pair | ¹²³I (SPECT) | ⁶⁸Ga-DOTATATE (PET) | No direct pair
Comparative Summary of the 3 TRT Agents

## Slide 24
Challenges & Perspectives
11/05/2026
Dose Optimization (ALARA, inverse planning)
Spatial Precision (IGRT, respiratory gating)
Radiation Protection (shielding, zoning, risks)
4) CHALLENGES AND FUTURE PERSECTIVES:
Dose Optimization
Main Challenge
•High dose → toxicity & healthy tissue damage
•Low dose → poor image quality or ineffective treatment
Key Concepts
•ALARA principle (As Low As Reasonably Achievable)
•Inverse planning
Maximum dose to organs at risk (OAR)
Minimum dose to the tumor
•Optimization algorithms → balance between:
tumor coverage
healthy tissue protection
Goal​
Deliver the most effective dose while minimizing biological risks.​
​

## Slide 25
Challenges & Perspectives
11/05/2026
Spatial Precision
Main Challenges
•Patient motion
•Internal organ motion (breathing, organs)
Advanced Techniques
•IGRT (Image-Guided Radiotherapy) → real-time imaging for accurate positioning
•Respiratory gating → synchronization with the breathing cycle
•PTV safety margins → compensate for uncertainties and motion
Goal
Increase tumor targeting accuracy while protecting healthy tissues.

## Slide 26
Challenges & Perspectives
11/05/2026
Spatial Precision
Respiratory gating
PTV safety margins

## Slide 27
Challenges & Perspectives
11/05/2026
Radiation Protection
Fundamental Principles
Time → reduce exposure duration
Distance → stay away from the source
Shielding → lead, concrete barriers
Radiation Risks
Deterministic effects (burns, tissue damage)
Stochastic effects (cancer risk)
Main Objectives​
Protect patients ​
Protect medical staff ​
Reduce environmental impact ​
Goal​
Minimize radiation risks while maintaining medical effectiveness.

## Slide 28
Future Perspectives
11/05/2026
Future Perspectives
Theranostics
•Same molecule for diagnosis & therapy
•Tracer + therapeutic radionuclide
•Personalized medicine
Artificial Intelligence
•Automatic treatment optimization
•Improved image reconstruction
•Clinical decision support
Nanoparticles
Targeted delivery to tumor cells
Localized dose delivery
Reduced side effects
Future Goal​
Towards more precise and personalized nuclear medicine.​

## Slide 29
General Conclusion
11/05/2026
General Conclusion
•Nuclear physics plays a major role in modern medicine
•Applications in imaging and therapy improve diagnosis and treatment
•Major challenges:
•dose optimization
•spatial precision
•radiation protection
•Future perspectives:
•theranostics
•artificial intelligence
•personalized medicine
•Toward safer, smarter, and more precise healthcare